## Slide 1: Chapter 2
Instructions: Language of the Computer

## Slide 2: Instruction Set
The repertoire of instructions of a computer
Different computers have different instruction sets
  But with many aspects in common
Early computers had very simple instruction sets
  Simplified implementation
Many modern computers also have simple instruction sets
§2.1 Introduction

## Slide 3: The MIPS Instruction Set
Used as the example throughout the book
Stanford MIPS commercialized by MIPS Technologies (www.mips.com)
Large share of embedded core market
  Applications in consumer electronics, network/storage equipment, cameras, printers, …
Typical of many modern ISAs
  See MIPS Reference Data tear-out card, and Appendixes B and E

## Slide 4: Arithmetic Operations
Add and subtract, three operands
  Two sources and one destination
add a, b, c # a gets b + c
All arithmetic operations have this form
Design Principle 1: Simplicity favours regularity
  Regularity makes implementation simpler
  Simplicity enables higher performance at lower cost
§2.2 Operations of the Computer Hardware

## Slide 5: Arithmetic Example
C code:
f = (g + h) - (i + j);
Compiled MIPS code:
add t0, g, h # temp t0 = g + h add t1, i, j # temp t1 = i + j sub f, t0, t1 # f = t0 - t1

## Slide 6: Register Operands
Arithmetic instructions use register operands
MIPS has a 32 × 32-bit register file
  Use for frequently accessed data
  Numbered 0 to 31
  32-bit data called a “word”
Assembler names
  $t0, $t1, …, $t9 for temporary values
  $s0, $s1, …, $s7 for saved variables
Design Principle 2: Smaller is faster
  c.f. main memory: millions of locations
§2.3 Operands of the Computer Hardware

## Slide 7
Some MIPS ISA Registers |  | 
Number | Reference | Use
0 | $zero | constant 0
1 | $at | reserved for assembler
2-3 | $v0-$v1 | function return values
4-7 | $a0-$a3 | arguments 1-4
8-15 | $t0-$t7 | temporary
16-23 | $s0-$s7 | saved
24-25 | $t8-$t9 | temporary
26-27 | $k0-$k1 | reserved for OS kernel
28 | $gp | pointer to global area
29 | $sp | stack pointer
30 | $fp | frame pointer
31 | $ra | fn call return address
HI | special | hi-order product; remainder
LO | special | lo-order product; dividend
PC | special | program counter
Notes: Some, because doesn’t include all of the registers, e.g., floating point registers. Above are mostly integer/fixed point

## Slide 8: Register Operand Example
C code:
f = (g + h) - (i + j);
  f, …, j in $s0, …, $s4
Compiled MIPS code:
add $t0, $s1, $s2 add $t1, $s3, $s4 sub $s0, $t0, $t1

## Slide 9: Memory Operands
Main memory used for composite data
  Arrays, structures, dynamic data
To apply arithmetic operations
  Load values from memory into registers
  Store result from register to memory
Memory is byte addressed
  Each address identifies an 8-bit byte
Words are aligned in memory
  Address must be a multiple of 4
MIPS is Big Endian
  Most-significant byte at least address of a word
  c.f. Little Endian: least-significant byte at least address

## Slide 10: Memory Operand Example 1
C code:
g = h + A[8];
  g in $s1, h in $s2, base address of A in $s3
Compiled MIPS code:
  Index 8 requires offset of 32
    4 bytes per word
lw $t0, 32($s3) # load word add $s1, $s2, $t0
offset
base register

## Slide 11: Memory Operand Example 2
C code:
A[12] = h + A[8];
  h in $s2, base address of A in $s3
Compiled MIPS code:
  Index 8 requires offset of 32
lw $t0, 32($s3) # load word add $t0, $s2, $t0 sw $t0, 48($s3) # store word

## Slide 12: Registers vs. Memory
Registers are faster to access than memory
Operating on memory data requires loads and stores
  More instructions to be executed
Compiler must use registers for variables as much as possible
  Only spill to memory for less frequently used variables
  Register optimization is important!

## Slide 13: Immediate Operands
Constant data specified in an instruction
addi $s3, $s3, 4
No subtract immediate instruction
  Just use a negative constant
  addi $s2, $s1, -1
Design Principle 3: Make the common case fast
  Small constants are common
  Immediate operand avoids a load instruction

## Slide 14: The Constant Zero
MIPS register 0 ($zero) is the constant 0
  Cannot be overwritten
Useful for common operations
  E.g., move between registers
  add $t2, $s1, $zero

## Slide 15: Unsigned Binary Integers
Given an n-bit number
Range: 0 to +2n – 1
Example
  0000 0000 0000 0000 0000 0000 0000 10112 = 0 + … + 1×23 + 0×22 +1×21 +1×20 = 0 + … + 8 + 0 + 2 + 1 = 1110
Using 32 bits
  0 to +4,294,967,295
§2.4 Signed and Unsigned Numbers

## Slide 16: 2s-Complement Signed Integers
Given an n-bit number
Range: –2n – 1 to +2n – 1 – 1
Example
  1111 1111 1111 1111 1111 1111 1111 11002 = –1×231 + 1×230 + … + 1×22 +0×21 +0×20 = –2,147,483,648 + 2,147,483,644 = –410
Using 32 bits
  –2,147,483,648 to +2,147,483,647

## Slide 17: 2s-Complement Signed Integers
Bit 31 is sign bit
  1 for negative numbers
  0 for non-negative numbers
–(–2n – 1) can’t be represented
Non-negative numbers have the same unsigned and 2s-complement representation
Some specific numbers
  0: 0000 0000 … 0000
  –1: 1111 1111 … 1111
  Most-negative: 1000 0000 … 0000
  Most-positive: 0111 1111 … 1111

## Slide 18: Signed Negation
Complement and add 1
  Complement means 1 → 0, 0 → 1
Example: negate +2
  +2 = 0000 0000 … 00102
  –2 = 1111 1111 … 11012 + 1 = 1111 1111 … 11102

## Slide 19: Sign Extension
Representing a number using more bits
  Preserve the numeric value
In MIPS instruction set
  addi: extend immediate value
  lb, lh: extend loaded byte/halfword
  beq, bne: extend the displacement
Replicate the sign bit to the left
  c.f. unsigned values: extend with 0s
Examples: 8-bit to 16-bit
  +2: 0000 0010 => 0000 0000 0000 0010
  –2: 1111 1110 => 1111 1111 1111 1110

## Slide 20: Representing Instructions
Instructions are encoded in binary
  Called machine code
MIPS instructions
  Encoded as 32-bit instruction words
  Small number of formats encoding operation code (opcode), register numbers, …
  Regularity!
Register numbers
  $t0 – $t7 are reg’s 8 – 15
  $t8 – $t9 are reg’s 24 – 25
  $s0 – $s7 are reg’s 16 – 23
§2.5 Representing Instructions in the Computer

## Slide 21: MIPS R-format Instructions
Instruction fields
  op: operation code (opcode)
  rs: first source register number
  rt: second source register number
  rd: destination register number
  shamt: shift amount (00000 for now)
  funct: function code (extends opcode)
op
rs
rt
rd
shamt
funct
6 bits
6 bits
5 bits
5 bits
5 bits
5 bits

## Slide 22: R-format Example
add $t0, $s1, $s2
special
$s1
$s2
$t0
0
add
0
17
18
8
0
32
000000
10001
10010
01000
00000
100000
000000100011001001000000001000002 = 0232402016
op
rs
rt
rd
shamt
funct
6 bits
6 bits
5 bits
5 bits
5 bits
5 bits

## Slide 23: Hexadecimal
Base 16
  Compact representation of bit strings
  4 bits per hex digit
0 | 0000 | 4 | 0100 | 8 | 1000 | c | 1100
1 | 0001 | 5 | 0101 | 9 | 1001 | d | 1101
2 | 0010 | 6 | 0110 | a | 1010 | e | 1110
3 | 0011 | 7 | 0111 | b | 1011 | f | 1111
Example: eca8 6420
  1110 1100 1010 1000 0110 0100 0010 0000

## Slide 24: MIPS I-format Instructions
Immediate arithmetic and load/store instructions
  rt: destination or source register number
  Constant: –215 to +215 – 1
  Address: offset added to base address in rs
Design Principle 4: Good design demands good compromises
  Different formats complicate decoding, but allow 32-bit instructions uniformly
  Keep formats as similar as possible
op
rs
rt
constant or address
6 bits
5 bits
5 bits
16 bits

## Slide 25: Stored Program Computers
Instructions represented in binary, just like data
Instructions and data stored in memory
Programs can operate on programs
  e.g., compilers, linkers, …
Binary compatibility allows compiled programs to work on different computers
  Standardized ISAs
The BIG Picture

## Slide 26: Logical Operations
Instructions for bitwise manipulation
Operation | C | Java | MIPS
Shift left | << | << | sll
Shift right | >> | >>> | srl
Bitwise AND | & | & | and, andi
Bitwise OR | ¦ | ¦ | or, ori
Bitwise NOT | ~ | ~ | nor
Useful for extracting and inserting groups of bits in a word
§2.6 Logical Operations

## Slide 27: Shift Operations
shamt: how many positions to shift
Shift left logical
  Shift left and fill with 0 bits
  sll by i bits multiplies by 2i
Shift right logical
  Shift right and fill with 0 bits
  srl by i bits divides by 2i (unsigned only)
op
rs
rt
rd
shamt
funct
6 bits
6 bits
5 bits
5 bits
5 bits
5 bits

## Slide 28: AND Operations
Useful to mask bits in a word
  Select some bits, clear others to 0
and $t0, $t1, $t2
0000 0000 0000 0000 0000 1101 1100 0000
0000 0000 0000 0000 0011 1100 0000 0000
$t2
$t1
0000 0000 0000 0000 0000 1100 0000 0000
$t0

## Slide 29: OR Operations
Useful to include bits in a word
  Set some bits to 1, leave others unchanged
or $t0, $t1, $t2
0000 0000 0000 0000 0000 1101 1100 0000
0000 0000 0000 0000 0011 1100 0000 0000
$t2
$t1
0000 0000 0000 0000 0011 1101 1100 0000
$t0

## Slide 30: NOT Operations
Useful to invert bits in a word
  Change 0 to 1, and 1 to 0
MIPS has NOR 3-operand instruction
  a NOR b == NOT ( a OR b )
nor $t0, $t1, $zero
0000 0000 0000 0000 0011 1100 0000 0000
$t1
1111 1111 1111 1111 1100 0011 1111 1111
$t0
Register 0: always read as zero

## Slide 31: Conditional Operations
Branch to a labeled instruction if a condition is true
  Otherwise, continue sequentially
beq rs, rt, L1
  if (rs == rt) branch to instruction labeled L1;
bne rs, rt, L1
  if (rs != rt) branch to instruction labeled L1;
j L1
  unconditional jump to instruction labeled L1
§2.7 Instructions for Making Decisions

## Slide 32: Compiling If Statements
C code:
if (i==j) f = g+h; else f = g-h;
  f, g, … in $s0, $s1, …
Compiled MIPS code:
bne $s3, $s4, Else add $s0, $s1, $s2 j Exit Else: sub $s0, $s1, $s2 Exit: …
Assembler calculates addresses

## Slide 33: Compiling Loop Statements
C code:
while (save[i] == k) i += 1;
  i in $s3, k in $s5, address of save in $s6
Compiled MIPS code:
Loop: sll $t1, $s3, 2 add $t1, $t1, $s6 lw $t0, 0($t1) bne $t0, $s5, Exit addi $s3, $s3, 1 j Loop Exit: …

## Slide 34: Basic Blocks
A basic block is a sequence of instructions with
  No embedded branches (except at end)
  No branch targets (except at beginning)
A compiler identifies basic blocks for optimization
An advanced processor can accelerate execution of basic blocks

## Slide 35: More Conditional Operations
Set result to 1 if a condition is true
  Otherwise, set to 0
slt rd, rs, rt
  if (rs < rt) rd = 1; else rd = 0;
slti rt, rs, constant
  if (rs < constant) rt = 1; else rt = 0;
Use in combination with beq, bne
  slt $t0, $s1, $s2 # if ($s1 < $s2) bne $t0, $zero, L # branch to L

## Slide 36: Branch Instruction Design
Why not blt, bge, etc?
Hardware for <, ≥, … slower than =, ≠
  Combining with branch involves more work per instruction, requiring a slower clock
  All instructions penalized!
beq and bne are the common case
This is a good design compromise

## Slide 37: Signed vs. Unsigned
Signed comparison: slt, slti
Unsigned comparison: sltu, sltui
Example
  $s0 = 1111 1111 1111 1111 1111 1111 1111 1111
  $s1 = 0000 0000 0000 0000 0000 0000 0000 0001
  slt $t0, $s0, $s1 # signed
    –1 < +1  $t0 = 1
  sltu $t0, $s0, $s1 # unsigned
    +4,294,967,295 > +1  $t0 = 0

## Slide 38: Procedure Calling
Steps required
  Place parameters in registers
  Transfer control to procedure
  Acquire storage for procedure
  Perform procedure’s operations
  Place result in register for caller
  Return to place of call
§2.8 Supporting Procedures in Computer Hardware

## Slide 39: Register Usage
$a0 – $a3: arguments (reg’s 4 – 7)
$v0, $v1: result values (reg’s 2 and 3)
$t0 – $t9: temporaries
  Can be overwritten by callee
$s0 – $s7: saved
  Must be saved/restored by callee
$gp: global pointer for static data (reg 28)
$sp: stack pointer (reg 29)
$fp: frame pointer (reg 30)
$ra: return address (reg 31)

## Slide 40: Procedure Call Instructions
Procedure call: jump and link
jal ProcedureLabel
  Address of following instruction put in $ra
  Jumps to target address
Procedure return: jump register
jr $ra
  Copies $ra to program counter
  Can also be used for computed jumps
    e.g., for case/switch statements

## Slide 41: Leaf Procedure Example
C code:
int leaf_example (int g, h, i, j) { int f; f = (g + h) - (i + j); return f; }
  Arguments g, …, j in $a0, …, $a3
  f in $s0 (hence, need to save $s0 on stack)
  Result in $v0

## Slide 42: Leaf Procedure Example
MIPS code:
leaf_example: addi $sp, $sp, -4 sw $s0, 0($sp) add $t0, $a0, $a1 add $t1, $a2, $a3 sub $s0, $t0, $t1 add $v0, $s0, $zero lw $s0, 0($sp) addi $sp, $sp, 4 jr $ra
Save $s0 on stack
Procedure body
Restore $s0
Result
Return

## Slide 43: Non-Leaf Procedures
Procedures that call other procedures
For nested call, caller needs to save on the stack:
  Its return address
  Any arguments and temporaries needed after the call
Restore from the stack after the call

## Slide 44: Non-Leaf Procedure Example
C code:
int fact (int n) { if (n < 1) return f; else return n * fact(n - 1); }
  Argument n in $a0
  Result in $v0

## Slide 45: Non-Leaf Procedure Example
MIPS code:
fact: addi $sp, $sp, -8 # adjust stack for 2 items sw $ra, 4($sp) # save return address sw $a0, 0($sp) # save argument slti $t0, $a0, 1 # test for n < 1 beq $t0, $zero, L1 addi $v0, $zero, 1 # if so, result is 1 addi $sp, $sp, 8 # pop 2 items from stack jr $ra # and return L1: addi $a0, $a0, -1 # else decrement n jal fact # recursive call lw $a0, 0($sp) # restore original n lw $ra, 4($sp) # and return address addi $sp, $sp, 8 # pop 2 items from stack mul $v0, $a0, $v0 # multiply to get result jr $ra # and return

## Slide 46: Local Data on the Stack
Local data allocated by callee
  e.g., C automatic variables
Procedure frame (activation record)
  Used by some compilers to manage stack storage

## Slide 47: Memory Layout
Text: program code
Static data: global variables
  e.g., static variables in C, constant arrays and strings
  $gp initialized to address allowing ±offsets into this segment
Dynamic data: heap
  E.g., malloc in C, new in Java
Stack: automatic storage

## Slide 48: Character Data
Byte-encoded character sets
  ASCII: 128 characters
    95 graphic, 33 control
  Latin-1: 256 characters
    ASCII, +96 more graphic characters
Unicode: 32-bit character set
  Used in Java, C++ wide characters, …
  Most of the world’s alphabets, plus symbols
  UTF-8, UTF-16: variable-length encodings
§2.9 Communicating with People

## Slide 49: Byte/Halfword Operations
Could use bitwise operations
MIPS byte/halfword load/store
  String processing is a common case
lb rt, offset(rs) lh rt, offset(rs)
  Sign extend to 32 bits in rt
lbu rt, offset(rs) lhu rt, offset(rs)
  Zero extend to 32 bits in rt
sb rt, offset(rs) sh rt, offset(rs)
  Store just rightmost byte/halfword

## Slide 50: String Copy Example
C code (naïve):
  Null-terminated string
void strcpy (char x[], char y[]) { int i; i = 0; while ((x[i]=y[i])!='\0') i += 1; }
  Addresses of x, y in $a0, $a1
  i in $s0

## Slide 51: String Copy Example
MIPS code:
strcpy: addi $sp, $sp, -4 # adjust stack for 1 item sw $s0, 0($sp) # save $s0 add $s0, $zero, $zero # i = 0 L1: add $t1, $s0, $a1 # addr of y[i] in $t1 lbu $t2, 0($t1) # $t2 = y[i] add $t3, $s0, $a0 # addr of x[i] in $t3 sb $t2, 0($t3) # x[i] = y[i] beq $t2, $zero, L2 # exit loop if y[i] == 0 addi $s0, $s0, 1 # i = i + 1 j L1 # next iteration of loop L2: lw $s0, 0($sp) # restore saved $s0 addi $sp, $sp, 4 # pop 1 item from stack jr $ra # and return

## Slide 52: 32-bit Constants
0000 0000 0111 1101 0000 0000 0000 0000
Most constants are small
  16-bit immediate is sufficient
For the occasional 32-bit constant
lui rt, constant
  Copies 16-bit constant to left 16 bits of rt
  Clears right 16 bits of rt to 0
lhi $s0, 61
0000 0000 0111 1101 0000 1001 0000 0000
ori $s0, $s0, 2304
§2.10 MIPS Addressing for 32-Bit Immediates and Addresses

## Slide 53: Branch Addressing
Branch instructions specify
  Opcode, two registers, target address
Most branch targets are near branch
  Forward or backward
op
rs
rt
constant or address
6 bits
5 bits
5 bits
16 bits
PC-relative addressing
  Target address = PC + offset × 4
  PC already incremented by 4 by this time

## Slide 54: Jump Addressing
Jump (j and jal) targets could be anywhere in text segment
  Encode full address in instruction
op
address
6 bits
26 bits
(Pseudo)Direct jump addressing
  Target address = PC31…28 : (address × 4)

## Slide 55: Target Addressing Example
Loop code from earlier example
  Assume Loop at location 80000
Loop: sll $t1, $s3, 2 | 80000 | 0 | 0 | 19 | 9 | 4 | 0
add $t1, $t1, $s6 | 80004 | 0 | 9 | 22 | 9 | 0 | 32
lw $t0, 0($t1) | 80008 | 35 | 9 | 8 | 0 |  | 
bne $t0, $s5, Exit | 80012 | 5 | 8 | 21 | 2 |  | 
addi $s3, $s3, 1 | 80016 | 8 | 19 | 19 | 1 |  | 
j Loop | 80020 | 2 | 20000 |  |  |  | 
Exit: … | 80024 |  |  |  |  |  | 

## Slide 56: Branching Far Away
If branch target is too far to encode with 16-bit offset, assembler rewrites the code
Example
  beq $s0,$s1, L1
  ↓
  bne $s0,$s1, L2 j L1 L2: …

## Slide 57: Addressing Mode Summary

## Slide 58: Synchronization
Two processors sharing an area of memory
  P1 writes, then P2 reads
  Data race if P1 and P2 don’t synchronize
    Result depends of order of accesses
Hardware support required
  Atomic read/write memory operation
  No other access to the location allowed between the read and write
Could be a single instruction
  E.g., atomic swap of register ↔ memory
  Or an atomic pair of instructions
§2.11 Parallelism and Instructions: Synchronization

## Slide 59: Synchronization in MIPS
Load linked: ll rt, offset(rs)
Store conditional: sc rt, offset(rs)
  Succeeds if location not changed since the ll
    Returns 1 in rt
  Fails if location is changed
    Returns 0 in rt
Example: atomic swap (to test/set lock variable)
  try: add $t0,$zero,$s4 ;copy exchange value
  ll $t1,0($s1) ;load linked
  sc $t0,0($s1) ;store conditional
  beq $t0,$zero,try ;branch store fails
  add $s4,$zero,$t1 ;put load value in $s4

## Slide 60: Translation and Startup
Many compilers produce object modules directly
Static linking
§2.12 Translating and Starting a Program

## Slide 61: Assembler Pseudoinstructions
Most assembler instructions represent machine instructions one-to-one
Pseudoinstructions: figments of the assembler’s imagination
move $t0, $t1 → add $t0, $zero, $t1
blt $t0, $t1, L → slt $at, $t0, $t1 bne $at, $zero, L
  $at (register 1): assembler temporary

## Slide 62: Producing an Object Module
Assembler (or compiler) translates program into machine instructions
Provides information for building a complete program from the pieces
  Header: described contents of object module
  Text segment: translated instructions
  Static data segment: data allocated for the life of the program
  Relocation info: for contents that depend on absolute location of loaded program
  Symbol table: global definitions and external refs
  Debug info: for associating with source code

## Slide 63: Linking Object Modules
Produces an executable image
  1. Merges segments
  2. Resolve labels (determine their addresses)
  3. Patch location-dependent and external refs
Could leave location dependencies for fixing by a relocating loader
  But with virtual memory, no need to do this
  Program can be loaded into absolute location in virtual memory space

## Slide 64: Loading a Program
Load from image file on disk into memory
  1. Read header to determine segment sizes
  2. Create virtual address space
  3. Copy text and initialized data into memory
    Or set page table entries so they can be faulted in
  4. Set up arguments on stack
  5. Initialize registers (including $sp, $fp, $gp)
  6. Jump to startup routine
    Copies arguments to $a0, … and calls main
    When main returns, do exit syscall

## Slide 65: Fallacies
Powerful instruction  higher performance
  Fewer instructions required
  But complex instructions are hard to implement
    May slow down all instructions, including simple ones
  Compilers are good at making fast code from simple instructions
Use assembly code for high performance
  But modern compilers are better at dealing with modern processors
  More lines of code  more errors and less productivity
§2.18 Fallacies and Pitfalls

## Slide 66: Fallacies
Backward compatibility  instruction set doesn’t change
  But they do accrete more instructions
x86 instruction set

## Slide 67: Pitfalls
Sequential words are not at sequential addresses
  Increment by 4, not by 1!
Keeping a pointer to an automatic variable after procedure returns
  e.g., passing pointer back via an argument
  Pointer becomes invalid when stack popped

## Slide 68: Concluding Remarks
Design principles
  1. Simplicity favors regularity
  2. Smaller is faster
  3. Make the common case fast
  4. Good design demands good compromises
Layers of software/hardware
  Compiler, assembler, hardware
MIPS: typical of RISC ISAs
  c.f. x86
§2.19 Concluding Remarks

## Slide 69: Concluding Remarks
Measure MIPS instruction executions in benchmark programs
  Consider making the common case fast
  Consider compromises
Instruction class | MIPS examples | SPEC2006 Int | SPEC2006 FP
Arithmetic | add, sub, addi | 16% | 48%
Data transfer | lw, sw, lb, lbu, lh, lhu, sb, lui | 35% | 36%
Logical | and, or, nor, andi, ori, sll, srl | 12% | 4%
Cond. Branch | beq, bne, slt, slti, sltiu | 34% | 8%
Jump | j, jr, jal | 2% | 0%