## Slide 1: Introduction TO HIGH PERFORMANCE COMPUTING

## Slide 2: What Does performance mean?
It depends on what system we are talking about
Desktop Computers –
  Speed of execution is more important
Servers
  Throughput - the total amount of work
Ipad
  Power consumption becomes a factor

## Slide 3: Basic equation of system performance
Performance = 1 / Execution Time
In general – the faster a given task can be done, the better the system is said to perform

## Slide 4: calculating relative system performance
Performancex > Performancey
Execution Timex < Execution Timey
Performancex /Performancey = n
n is the relative performance

## Slide 5: Measuring system performance
Time is the measure of system performance
  Is it cpu time – time spent by the cpu on a specific task?
  Is it I/O time – time spent getting tasks into computer so that cpu can work on them?
System Performance – elapsed time that user experiences
CPU performance – cpu time spent on users task
  clock cycles

## Slide 6: Understanding cpu performance
Instruction performance
  Impact of the number of instructions required to do a specific task
  Varies between processor architectures
Clock Cycle per instruction
  Varies within a given processor
Clock Cycle Time

## Slide 7: Instruction performance
CPU clock cycles = Instructions for a program * average clock cycles per instruction

## Slide 8: Classic cpu performance Equation
CPU time = Instruction count *
          average clock cycles per instruction *
          clock cycle time

## Slide 9: Amdahl's LAw
Execution time after an improvement =
(Execution time affected by improvement /
Amount of improvement )
+ Execution time UNAFFECTED by improvement

## Slide 10: What is high performance computing?
Definition – High-performance computing (HPC) is the use of super computers and parallel processing techniques for solving complex computational problems. HPC technology focuses on developing parallel processing algorithms and systems by incorporating both administration and parallel computational techniques. High-performance computing is typically used for solving advanced problems and performing research activities through computer modeling, simulation and analysis. HPC systems have the ability to deliver sustained performance through the concurrent use of computing resources.
from techopedia.com

## Slide 11: EXAMPLES of applications
climate prediction, protein folding simulations, oil and gas discovery, defense and aerospace work, automotive design, financial forecasting, etc.
corporate data center that stores customer records, inventory management, and employee details.

## Slide 12: parallelism – the foundation of Hpc
Basically, doing things in parallel that typically had been done serially.

## Slide 13: comparison of hpc methodologies
Instruction level parallelism
Task level parallelism
Data level parallelism

## Slide 14: instruction level parallelism
MIPS five stages of operation:
  Instruction fetch
  Instruction decode / register fetch
  Execution
  Memory access / branch completion
  Write back

## Slide 15: super scalar cpu
Superscalar - allows multiple instructions to be executed per clock cycle by providing multiple copies of subunits

## Slide 16: pipelining
Sequencing unrelated activities such that they use different components at the same time.

## Slide 17: Putting the two together in MIPS

## Slide 18: characteristics
Implicit - programmer doesn’t need to do anything
Data independence is important and limits how well superscaling works.

## Slide 19: example
A R2 = R1 + 1
B R3 = R2 + R1 // uh oh data dependence
C R4 = R5 + R6
D BZ R2, G // branch to G if R2 == 0
E R3 = R7 + R2 // data dependence
F R9 = R4 +1
G R9 = R7 – R1 // output depends

## Slide 20: Task level parallelism

## Slide 21: Threading
What is a thread?
  A separate process with its own instructions and data
  Each thread has all the state (instructions, data, PC, register state, page table, ect.)
Can share memory via virtual memory
Hardware must support rapid switching

## Slide 22: Multithreading
A processor can execute multiple threads by “ switching” back and forth
Switching involves clearing shared resources and reloading these resources with the new thread
It is happening on the SAME processor!
It increases performance - BUT
It is in general NOT parallel processing!

## Slide 23: multiprocessing
Processors with multiple cores
Cores have all resources – may share cache
Each core can run a separate thread
This is task level parallelism

## Slide 24: characteristics
Operating system and programmer have a much bigger role in how this works
Programs can be optimized to be able to be split up and run on separate cores

## Slide 25: Example

## Slide 26: data level parallelism
Applying the same operations to multiple items of data in parallel

## Slide 27: characteristics
Use depends on having data where this is useful
Huge application in graphics processing

## Slide 28: example
Intel MMX
  64 bit registers that can be broken up in multiple ways.

## Slide 29: INTEL MMX