## Slide 1: Memory mapped i/0

## Slide 2: Communication
What is a bus?
  A bit highway that allows bits to move from one “functional unit” to another “functional unit” in the system.
Examples:
  PCI
  ISA
  SCSI
  USB

## Slide 3: What kinds of things use i/o
Examples of i/o devices
  Keyboard
  Disk Drive
  Mouse
  Cameras
  Microphone
  Scanner

## Slide 4: One bus – so many devices
I/O handler structure
The MIPS address space

## Slide 5: MIPS ADDRESS SPACE
Code
Data
Heap
Stack
OS
0x00400000
Memory Mapped I/O
0xffff0000
0x80000080
0x10040000
0xfffffffc

## Slide 6: I/O handler structure
Device busy/ready (1 = ready)
Control
Data
32 bits wide
0
1
2
3
4
5
6
0
32 bits wide
7

## Slide 7: Quick review of base addressing
Base addressing starts with a base address
Other addresses are referenced from this base address
lw $t1, 8($a3)
Contents of a3 is base address
loading word into address 8 bytes higher
The 8 is decimal not hex!

## Slide 8: Data Rates of different devices

## Slide 9: Implications of different speeds
In many cases, the devices are much slower than the cpus operating speed and any data sent to the processor is dealt with essentially instantly from the perspective of the external device.

## Slide 10: Dealing with Speed Differences
Polling
  Polling is a looping code structure
  The loop continues to read a variable/memory location until an expected change occurs and then the loop exits and some code execute

## Slide 11: memory mapped i/o on mips
Interacting with a keyboard and display

## Slide 12: Keyboard I/O in MIPS
Control
Data
0
1
2
3
4
5
6
0
7
0xffff0000
0xffff0004

## Slide 13: Reading from keyboard
    li $a3, 0xffff0000
CkReady:
    lw $t1, 0($a3) #read from control register
    andi $t1, $t1, 1 # extract ready bit
    beqz $t1, CkReady # if not ready repeat
    lw $t0, 4($a3) #get character from keyboard

## Slide 14: Display I/O in MIPS
Control
Data
0
1
2
3
4
5
6
0
7
0xffff0000
0xffff0004
Control
Data
0
1
2
3
4
5
6
0
7
0xffff0008
0xffff000c

## Slide 15: Writing to display
    li $a3, 0xffff0000
XReady:
    lw $t1, 8($a3) #read from control register
    andi $t1, $t1, 1 # extract ready bit
    beqz $t1, XReady # if not ready repeat
    sw $t0, 12($a3) #Send character to the display

## Slide 16: POLLING two input devices
How would we poll two input devices?

## Slide 17: Adding mouse
Control
Data
0
1
2
3
4
5
6
0
7
0xffff0000
0xffff0004
Control
Data
0
1
2
3
4
5
6
0
7
0xffff0008
0xffff000c
Control
Data
0
1
2
3
4
5
6
0
7
0xffff0010
0xffff0014
MOUSE
KEYBOARD

## Slide 18: example